## Slide 1
Autonomous Driving System in CARLA Simulator
CMPE 789 - Robot Perception Final Project
Presented by: Justin Mascarenhas
December 2025
1/18

## Slide 2
Project Overview
Introduction
Objective
Develop a fully autonomous driving system in CARLA 0.9.15:
• Navigate roads using ultra fast lane detection path planning
• Detect and respond to traffic elements
• Follow lane markings using deep learning
• Make real-time driving decisions
Key Components
• Perception: YOLO + UFLD
• Planning: Waypoint navigation
• Control: Speed & steering
Technologies
• CARLA 0.9.15 Simulator
• PyTorch / CUDA
• Ultralytics YOLO11
• Ultra Fast Lane Detection
2/18

## Slide 3
System Architecture
High-Level Pipeline
CARLA SIMULATOR
• RGB Camera (1640×590) → PERCEPTION MODULE
PERCEPTION MODULE
• YOLO11 Custom Object Detection: Vehicles, Pedestrians, Traffic Lights, Speed Signs
• UFLD Fine-tuned Lane Detection: Lane boundaries, Center line, Steering angle
DECISION MODULE
• Traffic Light Color Detection (HSV Analysis): Red/Yellow → STOP, Green → GO
• Speed Control: Max 20 km/h, Turn slowdown, Emergency stop
• Steering Control: Max ±70°, Normalized [-1, 1]
3/18

## Slide 4
Methodology
Step-by-Step Pipeline
1. Environment Setup
• Synchronous mode for determinism
• Fixed delta: 0.3s per tick
• Camera: 1640×590, 150° FOV
• Position: 1.5m forward, 2.4m height
2. Perception Pipeline
• Frame capture from RGB camera
• YOLO detection (conf > 0.3)
• UFLD lane detection
• Coordinate scaling (800×288 → 1640×590)
3. Decision Making
• Traffic light: HSV color detection
• Obstacle avoidance: Distance from bbox
• Steering: Lane-based vs waypoint-based
4. Control Execution
• Apply throttle, steering, brake
• Update waypoint tracking
• Update spectator camera view
4/18

## Slide 5
YOLO Object Detection
Custom YOLO11n Model
Model Architecture
• Base: YOLO11n (Nano) - fastest
• Input: 640×640 (auto-resized)
• Output: BBox + Class + Confidence
Distance Estimation
• Pinhole camera model
• distance = (real_height × focal) / bbox_height
Class ID | Class Name | Use Case
0 | vehicle | Collision avoidance
1 | pedestrian | Emergency stop
2 | traffic_light | Signal detection
3 | speed_limit | Speed regulation
5/18

## Slide 6
YOLO Training Pipeline
Dataset Generation & Training
Data Collection
• Automated collection in CARLA
• Multiple maps & weather conditions
• Various traffic densities
Dataset Structure
• yolo_carla_dataset_v2/
- images/train/, val/
- labels/train/, val/
- data.yaml
Training Parameters
• Epochs: 100
• Image size: 640×640
• Batch size: 32
• Optimizer: SGD with momentum
• LR: 0.01 with cosine decay
Dataset Stats
• Training: ~5000+ images
• Validation: ~1000+ images
• Balanced class distribution
6/18

## Slide 7
UFLD Lane Detection
Ultra Fast Lane Detection Model
Model Architecture
• Backbone: ResNet-18
• Input: 800×288 (resized)
• Output: Lane points as grid classifications
• Row Anchors: 56 rows in bottom 60%
Pre-trained Base
• Original: TuSimple (real-world)
• Fine-tuned: CARLA simulator data
Key Configuration
• img_w = 800, img_h = 288
• griding_num = 100
• cls_num_per_lane = 56
• num_lanes = 4
Coordinate Transform
• scale_x = 1640/800 = 2.05
• scale_y = 590/288 = 2.05
7/18

## Slide 8
UFLD Training Pipeline
Fine-tuning on CARLA Data
Data Capture Settings
• Camera: 1640×590, FOV=150°
• Capture interval: Every 10 frames
• Auto-pilot for diverse scenarios
Dataset Format (TuSimple)
• ufld_carla_dataset/
- clips/0530/.../20.jpg
- label_data_0530.json
- list/train_gt.txt, test_gt.txt
Training Config
• backbone = 'resnet18'
• epochs = 50, batch_size = 32
• learning_rate = 4e-4
• optimizer = Adam
Fine-tuning Strategy
1. Load pre-trained TuSimple weights
2. Freeze backbone (10 epochs)
3. Unfreeze, train end-to-end
4. Save best on validation acc
8/18

## Slide 9
Traffic Light Detection
HSV Color Analysis
Pipeline
1. YOLO detects traffic light bbox
2. Crop the detected region
3. Convert to HSV color space
4. Count pixels in each color range
5. Determine dominant color
Decision Logic
• If traffic light < 20m distance:
- Green → Continue driving
- Red/Yellow/Unknown → Full stop
HSV Ranges (CARLA-tuned)
Red (hue wraps at 0/180)
• H=[0-15], S=[70-255], V=[70-255]
• H=[160-180], S=[70-255], V=[70-255]
Yellow/Amber
• H=[16-40], S=[70-255], V=[70-255]
Green
• H=[40-90], S=[70-255], V=[70-255]
9/18

## Slide 10
Steering and Speed Control
Control System
Steering Calculation
• lateral_offset = point.x - center_x
• lane_angle = atan2(dx, dy)
• steering = angle + (offset/center)×15°
• Normalize to [-1, 1] via /75
Speed Control
• Base target: 20 km/h cap
Turn-aware Adjustment
• steering > 10° → 70% speed
Obstacle-based Modifier
• vehicle < 15m → scale by dist/15
Throttle/Brake
• Stop → throttle=0, brake=1
• Below target → throttle up
• Above target → brake
10/18

## Slide 11
Waypoint Navigation
Path Planning
Waypoint Generation
• Start from spawn point
• Get waypoints with 10m spacing
• Limited to 200 waypoints ahead
Waypoint Tracking
• Update when distance < 2.0m
• Calculate angle to next waypoint
• Use dot product with forward vector
Spectator Camera
• Follows ego vehicle from behind
• Position: 8m behind, 4m above
• Looks at vehicle location
Fallback Behavior
• If lanes not detected → waypoints
• If waypoints exhausted → regenerate
11/18

## Slide 12
Issues Faced & Solutions
Challenges Part 1
Challenge 1: Traffic Light Color Detection
• Problem: CARLA's red lights appeared orange; green sometimes detected as red
• Solution: Extended red hue range to 0-15, adjusted S/V thresholds to 70
Challenge 2: Lane Detection Coordinate Mismatch
• Problem: UFLD outputs at 800×288, camera is 1640×590 - lanes misaligned
• Solution: Scale all lane points by 2.05× in both X and Y directions
Challenge 3: GPU/CPU Fallback
• Problem: CUDA errors on some systems during inference
• Solution: Try-except with automatic CPU fallback for lane detector
12/18

## Slide 13
Issues Faced & Solutions
Challenges Part 2
Challenge 4: Lane Flickering at Intersections
• Problem: Multiple lanes detected at intersections, center line unstable
• Solution: Lane filtering with MAX_LANE_ANGLE=40°, MAX_ANGLE_DIFF=25°
Score-based lane pair selection with width constraints
Challenge 5: Steering Oscillation
• Problem: Lane steering caused zigzag driving, over-correction at small angles
• Solution: Threshold-based steering source: |angle| ≤ 5° → lane, else → waypoint
Challenge 6: Synchronization Issues
• Problem: Simulation running faster than perception processing, frame drops
• Solution: Synchronous mode with fixed_delta_seconds = 0.3, manual tick control
13/18

## Slide 14
Results & Demo
System Performance
Capabilities Demonstrated
✅ Autonomous waypoint navigation
✅ Lane following with center tracking
✅ Vehicle detection & distance estimation
✅ Pedestrian detection with emergency stop
✅ Traffic light color recognition
✅ Dynamic traffic (30+ vehicles, 10+ peds)
Parameter | Value
Max Speed | 20 km/h
Max Steering | ±70°
Steering Threshold | 5°
Safe Dist (Vehicle) | 15m
Safe Dist (Pedestrian) | 10m
Safe Dist (Traffic Light) | 20m
Command: python step5_full_system_v4.py --vehicles 30 --pedestrians 10
14/18

## Slide 15
Future Improvements
Potential Enhancements
Perception
• Add LiDAR for 3D detection
• Sensor fusion (Camera + LiDAR)
• BEVFormer for bird's eye view
Planning
• A* or RRT path planning
• Dynamic re-routing
• Multi-lane driving & lane changes
Control
• PID controller tuning
• Model Predictive Control (MPC)
• RL for end-to-end driving
Robustness
• Weather handling (rain, fog)
• Night driving with headlights
• More diverse training data
15/18

## Slide 16
Conclusion
Summary
What We Built
• Custom YOLO11 for CARLA objects
• Fine-tuned UFLD for lane detection
• HSV traffic light color recognition
• Lane-following navigation with fallback
• Real-time decision & vehicle control
Key Learnings
• Domain adaptation is crucial
• HSV tuning is environment-specific
• Coordinate transforms matter
• Synchronous mode essential
Technologies Mastered
• CARLA API, YOLO, UFLD
• OpenCV, PyTorch, Real-time systems
16/18

## Slide 17
References
Resources
Frameworks & Tools
• CARLA Simulator: https://carla.org/
• Ultralytics YOLO: https://docs.ultralytics.com/
• Ultra Fast Lane Detection: https://github.com/cfzd/Ultra-Fast-Lane-Detection
Papers
• YOLO: 'You Only Look Once: Unified, Real-Time Object Detection'
• UFLD: 'Ultra Fast Structure-aware Deep Lane Detection'
17/18

## Slide 18
Thank You!
Questions?
18/18